## Slide 1: Arista Programmability
eAPI | EosSdk | Python | PowerShell | C++

## Slide 2: Setup
Enable Hyper-V
Download and install Docker
  https://www.docker.com/products/docker#/windows
Download and Install GitHub for Windows ( optional )
Browse to:
  https://github.com/arista-northwest/arista-programmability
  Click Clone download and select “Open in Desktop”
  Or … “Download ZIP”
Base installation steps

## Slide 3: Docker build and run
Build the Container
PS> cd <path-to-projects>/arista-programmability
PS> docker build -t ubuntu:arista-prog .
Run and Connect
PS> docker run -it -v <path-to-projects>/arista-programmability:/opt/arista-prog `
ubuntu:arista-prog
What does this do?
“-it” runs the container interactively and allocates a tty (runs a shell)
“-v <loca-path>:<container-path>” mounts the specified directory inside the container
“ubuntu:arista-prog” is the tag (name) given at build time
Download the EosSdk-stubs to the project folder (link will be provided)

## Slide 4: vEOS + HyperV: A Love Story
I’ve bundled the PDF with this project…
Here’s the short version:
Download a vEOS-lab vmdk (please use 4.17.1.1F for this lab)
Use Mvmc to convert to VHD
Create VM
In settings:
  Delete SCSI and Network controllers
  Add Aboot as a CDROM
  Add legacy networking controllers

## Slide 5: eAPI: Basic Operation
aaa authorization exec default local
aaa authentication policy local allow-nopassword-remote-login
!
username admin privilege 15 role network-admin
!
management api http-commands
protocol http
no shutdown
Step 1: Enable eAPI + Bonus (in)security settings
Step 2: Verify on-switch @ http://<switch-addr>/explorer.html

## Slide 6: eAPI: Switch Based Script Editor
Edit JavaScript inline
Fully functional
Provide more advanced playground for testing with eAPI
Good reference if you know JavaScript
  Further reading: http://<switch-addr>/main.js

## Slide 7: eAPI: Basic Python Usage
NO additional libraries are required!
endpoint ="http://{}/command-api".format(switch_addr)
payload = magic_payload_constructing_function(commands)
headers = {"Content-Type": "application/json"}
creds = (username, password)
req = urllib2.Request(endpoint)
req.add_header("Content-Type",)
password_manager = urllib2.HTTPPasswordMgrWithDefaultRealm()
password_manager.add_password(None, endpoint, creds[0], creds[1])
auth_manager = urllib2.HTTPBasicAuthHandler(password_manager)
opener = urllib2.build_opener(auth_manager)
urllib2.install_opener(opener)
handler = urllib2.urlopen(req, data=payload)
See how easy that was!

## Slide 8: eAPI: Basic Python Usage (Second try)
endpoint = "http://{}/command-api".format(switch_addr)
payload = magic_payload_constructing_function(commands)
headers = {"Content-Type": "application/json"}
creds = (username, password)
# now make the request.
requests.post(endpoint,
auth=creds, headers=headers, data=payload)
Take away: don’t bother with urllib2 – use a wrapper like ‘requests’
Install required additional libraries: requests (or jsonrpclib)

## Slide 9: eAPI: Neat Tricks
Escape the CLI (Bash commands are supported)
  Caveat: you must specify a timeout
commands = ["show version", "bash timeout 30 uname -a"]
Supply input for prompted commands
commands = [{"cmd": "enable", "input": "s3cr3t"},
"show running-config"]

## Slide 10: Handling eAPI Responses
All eAPI responses are JSON formatted
print "The system hostname is:", response["result"][0]["hostname"]
Python handling code
{
"id": "AristaProgrammability-1",
"jsonrpc": "2.0",
"result": [
{
"fqdn": "localhost",
"hostname": "localhost"
}
]
}

## Slide 11: eAPI: Dealing with problems…
Traceback (most recent call last):
File "eapi_client.py", line 372, in <module>
main()
File "eapi_client.py", line 356, in main
response = client.send(commands)
File "eapi_client.py", line 288, in send
raise EapiException(response["error"]["message"])
__main__.EapiException: CLI command 1 of 1 'show venison' failed: invalid command
Traceback (most recent call last):
File "eapi_client.py", line 372, in <module>
main()
File "eapi_client.py", line 356, in main
response = client.send(commands)
File "eapi_client.py", line 290, in send
return response["result"]
KeyError: 'result'

## Slide 12: eAPI: Handling Errors
{
"id": "AristaProgrammability-1",
"jsonrpc": "2.0"
"error": {
"code": 1003,
"data": [
{
"errors": [
"Command cannot be used over the API at this time. \
To see ASCII output, set format='text' in your request"
]
}
],
"message": "CLI command 1 of 1 'show clock' failed: unconverted command"
},
}
Python handling sudo-code
if "error" in response:
# … evasive action …

## Slide 13: eAPI: Raising and Catching Exceptions
Continuing from previous slide… Here’s a complete error handler example
class EapiException(Exception):
"""This class definition only purpose is to give the exception a name"""
pass
def send_commands(client, commands):
response = do_eapi_stuff()
if "error" in response:
raise EapiException(response["error"]["message"])
try:
response = send_commands(client, bogus_commands)
# we will never get here if the commands are indeed bogus
print "RESPONSE_OK:", response
except EapiException as exc:
# catch the exception raised in side the function
print "ERROR:", exc.message

## Slide 14: PSA: Don’t Repeat Yourself (DRY)
Avoid repletion everywhere possible
Makes refactoring and fixing bugs much easier
Results in more readable software.

## Slide 15: eAPI: PowerShell Module
Handles JSON
Uses PowerShell pipeline
Supports selecting results
PS > $conn = New-EapiConnection -HostName myswitch -UserName admin -Password ""
PS > $conn | Invoke-EapiCommands "show version"
modelName : DCS-7508
internalVersion : 4.16.6M
systemMacAddress : 00:1c:73:3c:ce:b2
serialNumber : NAN132700420
memTotal : 15681448
bootupTimestamp : 1464903383.51
memFree : 10935184
version : 4.16.6M
architecture : i386
isIntlVersion : False
internalBuildId : 667e1c30-0ed0-42e6-bd25-53adc03180e5
hardwareRevision : 06.00

## Slide 16: EOSSDK
What for? An on-box agent to handle events (a reactor)
  Examples
    Stream system counters (see TerminAttr)
    Make run-time changes to routing tables, ACLs, etc.
    Reacting to congestion or denial of services attacks…
    Now I’m rambling… Just look here: https://github.com/aristanetworks/EosSdk/wiki

## Slide 17: EOSSDK Stubs Installation
Download the stubs
Copy the tar

## Slide 18: Agents and Sysdb
Sysdb
EOSSDK
LED Agent
CLI
Ribd
MyAgent
External agents talk to Sysdb through the SDK
They hide much of the complexity inside Sysdb
Interfaces are documented publicly

## Slide 19: EOSDK Agent Anatomy
Boilerplate -
Including the bare minimum
This agent only derives from agent_handler. There are many others. Ex.
intf_handler: reacts to oper_status, speed changes, etc.
timeout_handler: reacts to a expiring timer
The Constructor: Initializes the tracer and handlers
Main function: Instantiates the agent class and starts the event loop

## Slide 20: EOSDK: Anatomy (Cont.)
Reacting to the initialization event
Reacting to events…
Reacting to configuration
Reacting to “real” events (note: agent must be extended to derive from eos::intf_handler)

## Slide 21: EOSSDK: Hello World
Basic EosSdk agent components
  Main agent class
  Event loop
  Reactor methods… To which events should the agent react?
    Examples include: on_timeout, on_intf_status, on_config_option
EosSdk resources:
https://github.com/aristanetworks/EosSdk/wiki

## Slide 22: EosSdk: Configuring the demo agent
localhost#configure
localhost(config)#daemon HelloWorld
localhost(config-daemon-HelloWorld)#exec /mnt/flash/HelloWorld
localhost(config-daemon-HelloWorld)#no shutdown
This is an EosSdk application
! No dedicated sysdb profile, using default
localhost(config-daemon-HelloWorld)#show daemon
Agent: HelloWorld (running)
No configuration options stored.
Status:
Data Value
-------------- ---------------------------
greeting Welcome! What is your name?

## Slide 23: Debugging and Tracing
switch(config)#trace HelloWorld setting HelloWorldCppAgent/*cf
switch(config)#end
switch#trace monitor HelloWorld
--- Monitoring /var/log/agents/HelloWorld-18512 ---
===== Output from /mnt/flash/HelloWorld [] (PID=18512) started Oct 11 23:36:17.705501 ===
[AtimeLog] Initially use syscall
2016-10-11 23:36:19.036055 Using external Socket tbl://sysdb/+n
2016-10-11 23:36:19.036172 Using externally set fd: 7
2016-10-11 23:36:19.251405 18512 HelloWorldCppAgent 0 Initialized
2016-10-11 23:42:12.689513 18512 HelloWorldCppAgent 3 Saying hi to Jesse
In this example:
The tracer is set to monitor all trace levels for the HelloWorld agent
The name “HelloWorldCppAgent” comes from the tracer config inside the agent
“*cf” means monitor levels from 0 to 9

## Slide 24: EOSSDK: Software Defined Routing
Python based controller
C++ Switch agent
Controller uses SPF algorithm to calculate paths through the network
Relies heavily on MPLS nexthop-groups
Can’t demo in vEOS… 

## Slide 25: Resources
Github Repo: https://github.com/arista-northwest/arista-programmability